## Slide 1: World’s oldest regional salt seal in the Amadeus and Officer Basins: implications for subsalt helium and hydrocarbons
Peter Haines

## Slide 2: Talk outline
Helium introduction
Helium in hydrocarbon reservoirs
Geological requirements for commercial helium accumulations
Why Western Australia may a good place to explore
Amadeus Basin
Officer Basin
Conclusions

## Slide 3: Helium (He)
Helium properties
  Second lightest element
  Second most abundant element in visible universe
  Noble gas / inert
  Lowest boiling point (-269˚C)
Very high demand with numerous hi-tech uses
Primordial He mainly found in mantle; crustal He constantly generated by radioactive decay of U and Th (α-particle = He nucleus)
Highly mobile due to inertness and small atom size; most free He in the crust lost into space over geological time

## Slide 4: Helium in hydrocarbon reservoirs
Most commercial He a bi-product of hydrocarbon production; separated from waste gas stream (rare He-only wells)
Small concentrations (<<1%) can be economic, depending on infrastructure and markets
High concentrations (>1%) are rare
US first and biggest producer (since 1920s); stockpiled He (National Helium Reserve) in depleted Texas gas field until mid-1990s
Non-US production only significant since 1990s
Australia producing He from Bayu-Undan field offshore Bonaparte Basin since 2010 (~0.1% He at wellhead)

## Slide 5: Geological requirements for commercial helium accumulations
A He source: radiogenic U-Th bearing rocks in basement or within a basin
A migration pathway (access to gas phase in pore fluid)
A porous reservoir and trap (same as conventional hydrocarbons)
Excellent seal due to high mobility; best seals are salt (halite, anhydrite)
Lots of time because He generation/accumulation is very slow
Coexisting hydrocarbon source; but a prolific source may reduce He concentration
Therefore for highest He concentration (>1%) look in old basins with marginal hydrocarbon source rocks and intact salt seals over early formed traps (in US most production from Paleozoic fields with late Paleozoic salt seal)

## Slide 6: Relevance to WA?
Extensive old basins (Paleozoic, Neoproterozoic, and older)
Radiogenic basement common
Multiple old salt deposits including world’s oldest basin-scale salt deposits (~800 Ma) in Officer and Amadeus basins; possibly extending elsewhere in the Centralian Superbasin
Due to long periods of stability since the Paleozoic the salt has potential to seals traps dating from the Paleozoic or even Neoproterozoic

## Slide 7: Centralian Superbasin
Cambrian
Ediacaran
Cryogenian
Tonian
Neoproterozoic
541 Ma
~635 Ma
~720 Ma
1000 Ma
Mesoproterozoic
SS1
SS2
SS3
SS4
Super-
sequences
Inter-glacial marine package
Post-glacial marine package
Syntectonic siliciclastic package
Elatina (“Marinoan”) Glaciation
Sturt (“Sturtian”) Glaciation
glacial erosion / unconformity
glacial erosion / unconformity
Generalized succession
Basal siliciclastic package
Centralian Superbasin
Evaporite–carbonate–shale package
(Post mid-Cambrian omitted)
Tectonized Centralian
Superbasin under
Canning Basin
Modified from Munson 2013
NTGS Spec Pub 5

## Slide 8: Centralian Superbasin
Cambrian
Ediacaran
Cryogenian
Tonian
Neoproterozoic
541 Ma
~635 Ma
~720 Ma
1000 Ma
Mesoproterozoic
SS1
SS2
SS3
SS4
Super-
sequences
Syntectonic siliciclastic package
Generalized succession
Basal siliciclastic package
Centralian Superbasin
(Post mid-Cambrian omitted)
Inter-glacial marine package
Post-glacial marine package
Elatina (“Marinoan”) Glaciation
Sturt (“Sturtian”) Glaciation
glacial erosion / unconformity
Evaporite–carbonate–shale package
Salt ~800 Ma (halite/anhydrite)
?
?
?
?
?
?
?
?
?
?
?
Tectonized Centralian
Superbasin under
Canning Basin
Modified from Munson 2013
NTGS Spec Pub 5
?
glacial erosion / unconformity

## Slide 9
Amadeus – Officer Tonian correlations
Amadeus Basin
Bitter Springs Gp
Heavitree Fm,
Dean Qtz, Kulail Sst
Woolnough Member
Browne
Formation
Gillen Formation
Johnnys Creek Fm
Townsend
Quartzite
Loves Creek Fm
‘Gillen salt’
‘lower Browne salt’
‘upper Browne salt’
‘basal Gillen shale’
Lefroy Fm
Reservoir
Stromatolites
Hydrocarbon source
WA Officer Basin
Buldya Group
Wallara Formation
upper Buldya Group
Bitter Sp. Anomaly δ13C (~800 Ma)
?
Baicalia burra
Stromatolite Assemblage
Acaciella australica
Stromatolite Assemblage
Tungussia erecta
vvvvvvv
~753 Ma volcanics
Supersequence 1
?

## Slide 10: Centralian Superbasin
Cambrian
Ediacaran
Cryogenian
Tonian
Neoproterozoic
541 Ma
~635 Ma
~720 Ma
1000 Ma
Mesoproterozoic
SS1
SS2
SS3
SS4
Super-
sequences
Syntectonic siliciclastic package
Generalized succession
Basal siliciclastic package
Centralian Superbasin
(Post mid-Cambrian omitted)
Inter-glacial marine package
Post-glacial marine package
Elatina (“Marinoan”) Glaciation
Sturt (“Sturtian”) Glaciation
glacial erosion / unconformity
Evaporite–carbonate–shale package
Salt ~800 Ma (halite/anhydrite)
?
?
?
?
?
?
?
?
?
?
?
?
Tectonized Centralian
Superbasin under
Canning Basin
Modified from Munson 2013
NTGS Spec Pub 5
Dukas 1
Mt Kitty 1
Magee 1
Mulyawara 1
Kutjara 1
GSWA Empress 1A
GSWA Lancer 1
glacial erosion / unconformity
Kanpa 1A
Yowalga 3

## Slide 11
Centralian Superbasin
Heavitree Fm – Alice Springs, NT
Contorted Gillen Fm – Ellery Creek, NT
Gillen Fm gypsum – Ringwood Dome, NT
Eastern Amadeus Basin
Gillen Fm salt – Murphy 1 WCR
Lower Gillen Fm shale – NT
Salt in upper Gillen Formation
Sub-salt black shales in NT drill holes (TOC up to 1.8%: Jarrett et al., 2016) are assumed source of sub-salt gas flows in Magee 1 and Mt Kitty 1
Bitter Sp Gp
Heavitree Fm
salt
lower shale
Johnnys Creek Fm
Loves Creek Fm
Gillen Formation
sandstone

## Slide 12
Centralian Superbasin
Heavitree Fm – north
WA Amadeus Basin
Basal Gillen Fm shale – north
Basal Gillen Fm shale – south
Contorted Bitter Springs Group – Bonython Ra
Dean Quartzite – south
Stromatolites allow confident identification of Gillen Fm in WA
Abundant evidence of salt tectonics in WA; no salt at surface but salt seal probably preserved at depth
Lower Gillen Fm shales in southwest much thicker than in east Amadeus
Thick sub-salt reservoir; some outcrops in N are not strongly silicified

## Slide 13: Amadeus Basin
Mt Kitty 1 (2,295 m)
Santos 2014 (Central Petroleum tenement)
420 Mscfd from weathered/fractured granite
Nitrogen 61%
Methane 13% 18%
Ethane 4%
Hydrogen 11%
Helium 9%
Magee 1 (2,696 m)
Pacific Oil & Gas 1992
63.1 Mscfd from 4.5 m sst
Shale 0.5-0.8% TOC
Nitrogen 43.61%
Methane 30.58%
Ethane 5.96% 49.09%
Propane 1.94%
Butane+ 1.66%
Carbon dioxide 0.58%
Hydrogen 0.03%
Argon 0.46%
Helium 6.23%
Dukas 1
Santos 2019 (Central Pet ten.)
(Drilling suspended above
inferred reservoir)

## Slide 14: Amadeus Basin
Mt Kitty 1 (2,295 m)
Santos 2014 (Central Petroleum tenement)
420 Mscfd from weathered/fractured granite
Nitrogen 61%
Methane 13% 18%
Ethane 4%
Hydrogen 11%
Helium 9%
Magee 1 (2,696 m)
Pacific Oil & Gas 1992
63.1 Mscfd from 4.5 m sst
Shale 0.5-0.8% TOC
Nitrogen 43.61%
Methane 30.58%
Ethane 5.96% 49.09%
Propane 1.94%
Butane+ 1.66%
Carbon dioxide 0.58%
Hydrogen 0.03%
Argon 0.46%
Helium 6.23%
Dukas 1
Santos 2019 (Central Pet ten.)
(Drilling suspended above
inferred reservoir)
Prove existence of a subsalt gas-prone hydrocarbon system
Prove integrity of the salt seal
9% He (Mt Kitty 1) close to the upper limit from wells world-wide
Isotope analysis indicates predominantly crustal He source
Concentration of other radiogenic noble gas isotopes indicates trapping and accumulation since Neoproterozoic (McInnes et al, 2017)
Hydrogen content (Mt Kitty 1) possibly “results from either hydrocarbon oxidation or as an abiogenic breakdown product of hydrocarbons in the granite reservoir…” (McInnes et al, 2017)
Both wells uneconomic because of poor reservoir

## Slide 15: Amadeus Basin
Mt Kitty 1 (2,295 m)
Santos 2014 (Central Petroleum tenement)
420 Mscfd from weathered/fractured granite
Nitrogen 61%
Methane 13% 18%
Ethane 4%
Hydrogen 11%
Helium 9%
Magee 1 (2,696 m)
Pacific Oil & Gas 1992
63.1 Mscfd from 4.5 m sst
Shale 0.5-0.8% TOC
Nitrogen 43.61%
Methane 30.58%
Ethane 5.96% 49.09%
Propane 1.94%
Butane+ 1.66%
Carbon dioxide 0.58%
Hydrogen 0.03%
Argon 0.46%
Helium 6.23%
Too deep
No reservoir
Sub-salt reservoir
and shale thickens
Dukas 1
Santos 2019 (Central Pet ten.)
(Drilling suspended above
inferred reservoir)

## Slide 16
From Haines and Allen, 2019, WABS paper
salt
salt

## Slide 17: Centralian Superbasin
Cambrian
Ediacaran
Cryogenian
Tonian
Neoproterozoic
541 Ma
~635 Ma
~720 Ma
1000 Ma
Mesoproterozoic
SS1
SS2
SS3
SS4
Super-
sequences
Syntectonic siliciclastic package
Generalized succession
Basal siliciclastic package
Centralian Superbasin
(Post mid-Cambrian omitted)
Inter-glacial marine package
Post-glacial marine package
Elatina (“Marinoan”) Glaciation
Sturt (“Sturtian”) Glaciation
glacial erosion / unconformity
Evaporite–carbonate–shale package
Salt ~800 Ma (halite/anhydrite)
?
?
?
?
?
?
?
?
?
?
?
?
Tectonized Centralian
Superbasin under
Canning Basin
Modified from Munson 2013
NTGS Spec Pub 5
Dukas 1
Mt Kitty 1
Magee 1
Mulyawara 1
Kutjara 1
GSWA Empress 1A
GSWA Lancer 1
glacial erosion / unconformity
Kanpa 1A
Yowalga 3

## Slide 18: Centralian Superbasin
?
?
?
?
?
?
?
?
?
?
?
?
Tectonized Centralian
Superbasin under
Canning Basin
Modified from Munson 2013
NTGS Spec Pub 5
Dukas 1
Mt Kitty 1
Magee 1
Mulyawara 1
Kutjara 1
GSWA Empress 1A
GSWA Lancer 1
Kanpa 1A
Yowalga 3
SW
NE

## Slide 19: Centralian Superbasin
Western Officer Basin: Browne Formation in GSWA Lancer 1
salt
dolomite

## Slide 20: Centralian Superbasin
Western Officer Basin: Browne Formation in GSWA Lancer 1
Limited subsalt exploration
GSWA stratigraphic holes not drilled on identified structural traps, and drilled into thin succession west of basin depocentre where salt unit sits on basement with very little subsalt shale
Exploration wells Kanpa 1A drilled outside subsalt reservoir; Yowalga 3 didn’t reach subsalt reservoir (if present)
Subsalt shale and sandstone reservoir can be inferred farther east (outcrop evidence)
Exploration drilling in SA near WA border (Mulyawara 1, Kutjara 1) prove subsalt shale and sandstone present, and contain numerous but minor gas shows over this stratigraphy

## Slide 21: Conclusions
World’s oldest regional salt seal widespread in Amadeus and Officer Basins
Basins overlie radiogenic basement He source
Salt locally overlies thick sandstone reservoir and marginal gas-prone hydrocarbon source rocks
Salt-sealed traps likely formed early (Neoproterozoic & Paleozoic tectonics)
Ingredients thus in place for a world-class He province (challenges are remoteness, and lack of subsurface data)
Trapping of very high He concentration in gas proven in two eastern Amadeus Basin wells (though uncommercial due to poor reservoir)
Considerable opportunities in WA parts of Amadeus and Officer Basins